## Slide 1
September 5, 2024
Clean Heat standard potential study
FINAL results
Notes: .

## Slide 2: Agenda
Introductions
Project Summary
Major Changes from Final Draft Results
Modeling Methodology
  Scenario definitions
  Modeling process
  Act 18 Optimized scenario assumptions
Maximum Achievable Results
  RCI emission totals
  Societal costs and benefits
Act 18 Optimized Results
  RCI emission totals
  Societal costs and benefits
  Cumulative emissions by measure type and sector
  Cumulative emissions by measure cost-effectiveness
  Top measures by emissions reductions
  Low/moderate-income potential
Workforce
Other Sources of Funding
Notes: 2

## Slide 3: Introductions
Project team and staff
Project Team
  NV5: Overall potential study project manager
  Energy and Environmental Economics, Inc. (E3): Emerging fuels subject matter experts
Staff Intros
  NV5
    Ben Cartwright, Project Manager
    Matthew Socks, Senior Technical Director
    Cliff McDonald, Senior Consultant
    Griff Keating, Consultant
  E3
    Dr. Bill Wheatle, Emerging Fuels Technical Lead

## Slide 4: Project summary
Clean Heat Standard
  To support the goals of the Global Warming Solutions Act (GWSA), The Clean Heat Standard is intended to reduce greenhouse gas emissions in Vermont’s thermal sector through clean heat credits representing reduced emissions from clean heat measures.
Project Objective
  The potential study will quantify the technically achievable and maximum achievable and thermal resources, including economic potential for Vermont thermal sector resources which will inform the price and amount of clean heat measures.
  The study will also quantify an Act 18 optimized achievable scenario to meet the requirements of Act 18.
CAVEATS
  The model simplifies significant variation in project costs, savings, and scope. There are large uncertainties around adoption rates, future technologies and costs, availability of renewable/biofuels, and how the market price will respond to the above factors.
  Modeled potential scenarios do not reflect an implementation plan. Modeled costs are an upper boundary intended to inform the ultimate cost of the Clean Heat Standard. Significant uncertainty remains around how an implementation program will function, who will be the primary implementers, and what the market will respond to.

## Slide 5: Major Changes from Final Draft Results
Summary of Major Changes
Updates to 2021 Vermont Greenhouse Gas Inventory and Forecast (“VT GHGI”) methods and results:
  Retroactive removal of “non-road” emissions previously included in the residential, commercial, and industrial fuel use sector (“RCI”), or “thermal sector”
  This change resulted in lower RCI emissions values than previous reports
New RCI GWSA reduction targets:
  Model incorporated emissions reduction targets reflecting sectoral proportionality based on 2018 (0.7 MMT by 2030 and 1.7 MMT by 2050 relative to 1990).
Clean fuels (CF) assumptions updates:
  Consistent with historical treatment of renewable natural gas in VT GHGI, emissions factors for biofuels and renewable fuels set to zero for GWSA accounting.
  CF emissions factors for certain pathways based on median values for active projects CARB’s LCFS project database.
  Doubled assumed availability of certain CFs in early years (relative to previous population-weighted approach) which transitions to the population-weighted values over time to reflect more competition for the resource.

## Slide 6: Methodology
Potential Scenarios
Technical Potential
  Full technical potential of each measure without competition.
Maximum Achievable Potential
  Maximum adoption through idealized program design and incentives covering 100% of installed costs.
Act 18 Optimization
  Maximum achievable potential adjusted and optimized to meet Act 18 policy requirements.
Economic Potential
  Subset of Maximum Achievable and Act 18 Optimized potential that passes the VT Societal Cost Test. For reporting purposes only (i.e., opportunities are not removed from the analysis based on societal cost-effectiveness).
Scenarios for Clean Heat Standard Potential Analysis

## Slide 7: Methodology
Overview of MODELING Process
Characterize Measure Level Savings, Costs, and Lifetimes
Define
Applicable Market
Estimate Technical Potential
Apply Mutual Exclusivity and Interactive Impacts
Define Adoption Curves (Penetrations)
Estimate Maximum Achievable Potential
Estimate Act 18 Optimized Potential
Screen for Cost-Effectiveness
(VT SCT)

## Slide 8: Methodology
Modeling assumptions
Aggressive ramp in Maximum Achievable scenario would considerably front-load achievement, exacerbating workforce constraints and leading to highly variable program budgets over the analysis period.
Converted the Maximum Achievable adoption rates to constant annual values by diving the cumulative adoption by the number of years in the analysis period (limiting incremental annual adoption values such that they did not exceed the Maximum Achievable adoption values for the corresponding year in early years).
Per Act 18 requirements to prioritize low-income and moderate-income, assumed all LMI energy efficiency and fuel switching measures are adopted.
Ranked each measure in the order of cost per ton of lifetime lifecycle GHG emissions reductions and removed the most expensive measures from the portfolio until the total emissions reductions matched the 2050 GWSA targets in 2049.
The maximum allowable emissions for 2026-2029 were linearly interpolated between the 2023 historical emissions and the 2030 GWSA target. Likewise, the maximum allowable emissions for 2030-2049 were linearly interpolated between the 2030 target and the 2050 target.
Adoption values for clean fuels were adjusted downward in each year, starting with the most expensive pathway, until the resulting emissions just meet the interpolated goals in each year.
Act 18 Optimized Potential Assumptions

## Slide 9: Maximum achievable potential
Maximum Achievable scenario achieves a reduction in net RCI emissions relative to a 1990 baseline of 1.2MMT CO2e in 2029 and 1.9MMT in 2049.
“Net RCI Emissions” denotes the inclusion of increased Electricity Consumption sector emissions but impacts minimal due to slow ramp of fuel switching measure adoption and plummeting electric emissions rates.
Increased emissions from 1990 to 2023 slightly undercut achievement toward 2030 GWSA target
Maximum Achievable Net RCI Emissions and GWSA Targets

## Slide 10: Maximum achievable potential
Total Modeled Societal NET Benefits
The total societal net benefits (per the VT SCT) associated with the Maximum Achievable potential are $1.0B (2024$).
  “Net” societal benefits reflect total societal benefits less total societal costs.
  Benefits include avoided energy/fuel, capacity, and T&D costs; additional resource savings; externalities, and non-energy benefits
  Costs include measure costs (less deferred equipment replacement costs) and increased electric and/or fuel consumption

## Slide 11: Maximum achievable potential
Societal COSTs AND Benefits

## Slide 12: Maximum achievable potential
Due to lower barriers biofuels/renewable fuels represent the majority of the potential in early years.
As fuel switching and energy efficiency measures increase in adoption, clean fuels potential is partially displaced.
By 2049, fuel switching measures represent 71% of the cumulative emissions reduction potential.
Maximum Achievable Cumulative Annual GWSA Emissions Reduction by Measure Type

## Slide 13: ACT 18 OPTIMIZED potential
Act 18 Optimized scenario achieves a reduction in net RCI emissions relative to a 1990 baseline of 0.7MMT CO2e in 2029 and 1.7MMT in 2049.
“Net RCI Emissions” denotes the inclusion of increased Electricity Consumption sector emissions but impacts minimal due to slow ramp of fuel switching measure adoption and plummeting electric emissions rates.
Increased emissions from 1990 to 2023 slightly undercut achievement toward 2030 GWSA target.
Act 18 Optimized Net RCI Emissions and GWSA Targets

## Slide 14: ACT 18 Optimized potential
Total Modeled Societal NET Benefits
The total societal net benefits (per the VT SCT) associated with the Act 18 Optimized potential are $3.0B (2024$).
  “Net” societal benefits reflect total societal benefits less total societal costs.
  Benefits include avoided energy/fuel, capacity, and T&D costs; additional resource savings; externalities, and non-energy benefits
  Costs include measure costs (less deferred equipment replacement costs) and increased electric and/or fuel consumption

## Slide 15: ACT 18 Optimized potential
Societal Costs and Benefits

## Slide 16: ACT 18 Optimized potential
Societal Costs and Benefits
The majority of the net benefits are generated by avoided social economic and environmental damages and avoided fuel oil and propane consumption.
The majority of the costs are due to incremental measure costs and increased biofuels and renewable fuels consumption.
Note certain SCT cost categories that contribute to both costs and benefits have been combined into “net” column elements.

## Slide 17: ACT 18 OPTIMIZED potential
Figure presents program incentive spending only as optimized to achieve GWSA targets.
Incentive spending relatively flat over analysis period due to calibration to interpolated annual GWSA targets.
Important to note that spending on CF yields one year of emissions reductions whereas spending on EE/FS measures can yield 15-20 years of reductions.
Act 18 Optimized Incremental Annual Incentives by Measure Type

## Slide 18: ACT 18 OPTIMIZED potential
Relative to the Maximum Achievable scenario, Act 18 Optimized potential increases gradually to match interpolated GWSA targets.
Biofuels/renewable fuels represent the majority of the cumulative emissions reduction potential through 2035, then overtaken by fuel switching measures.
Act 18 Optimized Cumulative Annual GWSA Emissions Reduction by Measure Type

## Slide 19: ACT 18 OPTIMIZED potential
Mirroring the emissions inventory, residential has the highest long term emissions reduction potential, followed by commercial then industrial.
“Sector Neutral” potential served entirely by clean fuels. Given difficulty to electrify certain industrial end-uses, much of the clean fuels potential is likely to serve the industrial sector in later years.
Act 18 Optimized Cumulative Annual GWSA Emissions Reductions by Sector

## Slide 20: ACT 18 OPTIMIZED potential
Measure cost-effectiveness determined by the Vermont Societal Cost Test (VT SCT).
While the majority of EE and CF potential is cost-effective, much of the FS potential is not cost-effective.
In 2049, 62% of the identified Act 18 Optimized potential emissions reductions is cost-effective.
Act 18 Optimized Cumulative Annual GWSA Emissions Reduction by Measure Type and Cost Effectiveness

## Slide 21: Act 18 Optimized Potential
Top 10 RESIDENTIAL measures by CONTRIBUTION to REQUIRED 2050 RCI EMISSIONS REDUCTIONS
FS = Fuel Switching; CF = Clean Fuels; EE = Energy Efficiency

## Slide 22: Act 18 Optimized Potential
Top 10 C&I measures by CONTRIBUTION to REQUIRED 2050 RCI EMISSIONS REDUCTIONS
FS = Fuel Switching; CF = Clean Fuels; EE = Energy Efficiency

## Slide 23: Act 18 Optimized Potential
Top 10 SECTOR NEUTRAL measures by CONTRIBUTION to REQUIRED 2050 RCI EMISSIONS REDUCTIONS
FS = Fuel Switching; CF = Clean Fuels; EE = Energy Efficiency

## Slide 24: ACT 18 OPTIMIZED potential
Act 18 requires “[o]f their annual [clean heat credit] requirement, each obligated party shall retire at least 16 percent from customers with low income and an additional 16 percent from customers with low or moderate income.”
Act 18 Optimized scenario exceeds requirement for Moderate Income but falls short for Low Income.
Analysis assumes clean fuels potential is apportioned to segment and income category based on remaining conventional fuel consumption.
Act 18 Optimized Percent Total Cumulative Annual Lifecycle Emissions Reduction by Income Level

## Slide 25: Workforce development
Summary of thermal sector trades
VT’s Clean Energy Industry (2023): 18,156 workers, representing 6% of all jobs in the state
Nearly half of these workers were in the installation, maintenance and repair field
Difficulty in hiring; mainly due to competition with other industries and lack of experience
Mechanical, electrical, engineering and installation represented 90% of positions most difficult to hire
Year | % Reporting Very Difficult in Hiring
2020 | 34%
2021 | 46%
2022 | 52%
2023 | 67%
Source: 2023 Vermont Clean Energy Industry Report

## Slide 26: Workforce development
Workforce training organizations
Several organizations in VT provide continuing education training for HVAC trade workforce
  Heating & Cooling Contractors of Vermont (HCCV), Vermont Fuel Dealers Association (VFDA), Vermont Adult Learning, ReSOURCE, etc.
Training programs include heat pump installation, weatherization and EPA Section 608 Certification (refrigerant handling)
Interviews with training organizations cite funding as major barrier to increased participation
  First-year funding can be adequate, but lack of support exists to maintain programs
  Regional training can be difficult due to lower participation in rural areas
Employers use training to pre-vet employees
  High satisfaction from HVAC trade employers with level of student training/skillsets
  Workforce organizations have relationships with HVAC trades for placement

## Slide 27: Workforce development
Gaps in workforce – optimized results
Measure | Number of Current Workers (2023) | BAU Workers in 2030 | Optimized Workers in 2030 | BAU Workers in 2049 | Optimized Workers in 2049
Weatherization Single-family | 140 | 113 | 435 | 65 | 435
Residential Heat Pumps (Ductless) | 70 | 82 | 24 | 125 | 30
Weatherization Mfg. Home | 20 | 16 | 19 | 7 | 19
Residential Heat Pumps (Ducted) | 15 | 17 | 27 | 27 | 34
Commercial Heat Pumps (Ductless) | 10 | 11 | 11 | 16 | 13
Measures selected where existing data aligned with modeling data
Largest gap is in Weatherization workforce based on Act 18 Optimized results
Increased funding can help support gaps
  WAP Innovation Grant Programs
  IRA funding
Additional measures in final report

## Slide 28: Sources of Additional Funding
Federal IRA Funding & Tax Credits | Tier 3 Renewable Energy Standard | Existing Efficiency Spending
Inflation Reduction Act provided for programmatic funding and enhanced tax credits applicable to several clean heat measures Direct funding for the rebate programs were considered in full, while applicability factors for tax-credit eligible measures were developed In aggregate accounted for $111M | Tier 3 of the Renewable Energy Standard requires Distribution Utilities to implement "energy transformation projects" that reduce fossil fuel usage This spending contributes to CHS requirements We hold 2022 spending constant over the study period This accounts for a total of $334M | Energy Efficiency Utilities spend significant funds on rebates for measures that would be CHS eligible We took 2023 spending on these measures and held it constant for the study period This resulted in a total $538M of spending

## Slide 29: Sources of Additional Funding
LMI Weatherization Funding | Total Other Funding Sources | Pre-Wx & Pre-Elx Barriers
Federal funding for low-income weatherization has been a long standing contributor to weatherization activity in VT We hold current funding levels constant for the study period This accounts for a total of $489M | Adding up the previously mentioned funding sources, we get a supplemental funding of $1.47B | Pre-weatherization and pre-electrification barriers, such as knob-and-tube wiring and the need for electrical panel upgrades, represent potentially significant and uncertain costs in the pursuit of widespread decarbonization We did not incorporate these costs into the study, but initial data from like jurisdictions reflect a possible cost of up to $5,000 per house on average
Funding | Total Spending
Total EEU Budget Applicable to CHS | $ 537,711,405
Total IRA Funding (HOMES/HEEHRA) | $ 39,036,720
Total LMI Wx Funding | $ 488,540,028
Total Tier III RES Spending | $ 334,270,104
Federal Tax Credits | $ 72,200,216
Total | $ 1,471,758,473

## Slide 30: Final report and supplemental data
Detailed appendices with measure-level potential results are available for all scenarios
Final report, supplemental workbooks, and TAG feedback responses available on Public Service Department website:
  https://publicservice.vermont.gov/clean-heat-standard/public-service-department-thermal-sector-carbon-reduction-potential-study

## Slide 31
Matt Socks, Senior Technical Director
matthew.socks@nv5.com
Ben Cartwright, Senior Consultant Clean Energy
benjamin.cartwright@nv5.com

## Slide 32
APPENDIX

## Slide 33: Methodology
Modeling assumptions
Baseline is the existing condition
  "Like-for-Like" replacement assumed for when the existing equipment would have failed
Results represent gross savings (i.e., no Net-to-Gross Ratios applied)
Baseline forecasted energy use assumed to be flat over analysis period
CHS is envisioned as a tool to meet GWSA targets (consistent with GHG inventory accounting) but credits are quantified in annual lifecycle emissions reductions
  Wood heating uses a GWPbio factor of 0.30 to reflect VT forests
Renewable/biofuels fuels repurchased every year; however, electrified customers (or more generally, customers who have fuel switched) will not revert to fossil fuel-fired equipment
General Assumptions

## Slide 34: Methodology
Modeling assumptions
Technical Potential assumes all technologically feasible measures could be installed instantaneously
Assumes measures impacts persist over the entire analysis period
  Exception: Biofuels and renewables fuels which must be implemented annually
Results reflect measure-level technical potential without any consideration of competition (i.e., mutual exclusivity) and measure interactions.
Therefore, the measure-level potential is not additive.
Technical Potential is useful as a steppingstone to conducting Maximum Achievable and Act 18 Optimized scenarios.
Technical Potential Assumptions

## Slide 35: Methodology
Modeling assumptions
Reflects application of adoption curves considering market barriers.
Includes impacts of measure competition (i.e., mutual exclusivity) and interactions.
Maximum Achievable potential assumes incentive costs only and does not include administrative program costs.
Maximum Achievable analysis assumes program incentives cover 100% of the total installed costs
  Installed costs are total estimated equipment and labor costs associated a customer would pay for the installation of clean heat measures.
  Exception: Installed cost for biofuel/renewable fuel measures is calculated as the difference in retail cost between the baseline conventional and clean fuel.
  Note: Electric panel upgrades and pre-weatherization barriers costs are not considered in total installed costs.
Clean Fuels are disqualified if and when they exceed carbon intensity requirements of Act 18.
Maximum Achievable Potential Assumptions

## Slide 36: methodology
Modeling assumptions – Maximum achievable
Measure Loading Order
1. Energy Efficiency
2. Fuel Switching
3. Clean Fuels
Measure Loading Order Example #1
(Residential – SF Home, Space Heating)
Air Sealing
Insulation
Advanced Thermostats
Partial Electrification
Clean Fuels
Part-to-Full Electrification
Measure Loading Order Example #2
(Industrial – Mfg. Facility, Industrial Process)
Clean Fuels

## Slide 37: Methodology
Modeling assumptions
Uses the Vermont Societal Cost Test (SCT) as the primary test*
As the Clean Heat Standard does not have explicit cost-effectiveness requirements, the SCT is only applied to the Maximum Achievable and Act 18 Optimized potential to estimate the portion of the identified potential that is economic vs. uneconomic.
Results assume 2023 EPA projections of Social Cost of Carbon (SCC) under 2% discount rate
  Value of $190/metric ton in 2020 in 2020$
  Pending VT Climate Council adoption of EPA’s 2023 value
For the purposes of monetizing the impacts of avoided emissions, assumes lifecycle emissions factors
*Components of the VT SCT can be found in Section 2.4.2.1 ‘Vermont Societal Cost Test’ in the January 2023 Vermont Energy Efficiency Market Potential Study.
Economic Potential Assumptions